EL_03_TEST_Soft_starters_EN

| Soft starters |  |
| --- | --- |
| Applications |  |
| The ABC soft start - soft stop unit is a controller with 6 thyristors which is used for the torque-controlled soft starting and stopping of three-phase squirrel cage asynchronous motors in the power range between 4 and 1200 kW. |  |
| It offers soft starting and deceleration functions along with machine and motor protection functions as well as functions for communicating with control systems. The highperformance algorithms of the ABC contribute significantly to its robustness, safety and ease of setup. |  |
| The ABC soft start - soft stop unit is a cost-effective solution which can: reduce machine operating costs by reducing mechanical stress and improving machine availability, reduce the stress placed on the electrical distribution system by reducing line current peaks and voltage drops during motor starts. |  |
| The ABC comprises a built-in terminal which can be used to modify programming, adjustment or monitoring functions in order to adapt and customise the application to meet individual customer requirements. |  |
| Drive performance functions: exclusive ABC torque control, constant control of the torque supplied to the motor during acceleration and deceleration periods (significantly reducing pressure surges), facility for adjusting the ramp and the starting torque, the starter can be bypassed using a contactor at the end of the starting period whilst maintaining electronic protection (by-pass function), wide frequency tolerance for generator set power supplies, the starter can be connected to the motor delta terminals in series with each winding. |  |
| Machine and motor protection functions: built-in motor thermal protection, processing of information from PTC thermal probes, monitoring of the starting time, motor preheating function, protection against underloads and overcurrents during continuous operation. |  |

# Footnotes

ABC – вымышленная торговая марка